## Slide 1: Auto Focus Network

## Slide 2: High Level Block Diagram
XY Coordinates
Obtain XY tile coordinates via micro magellan surface
Choose Tiles
Determine which tiles to focus on
Capture 3 plane images
At each determined tile, capture full frame images from 3 different z planes
Gaps between z planes is predetermined
Break Images into super pixels
Calculate reciprocal Brenner Score
Filter Brenner Score
Divide each image into an array of sub areas dubbed ‘super pixels’
Calculate brenner score for each super pixel and take reciprocal of it
Brenner score is pixel(col, row) – pixel(col + n, row).
Filter out background super pixels via ‘Well Depth’
Make Focus Prediction
Take 3 point reciprocal brenner score, solve quad equation and solve for derivative = 0 to find projected focus position. Use Gauss-Jordan reduction to solve
Fit Plane
Fit best plane to all points (X,Y, Predicted focus z position)
Use outlier dampening loss function to best fit with
Populate Focus Map
Use Plane(XY coordinates) to determine Z position for focus map
Pop FM array with depth of focus across 1 FOV
Z value in FM is top value. Work down when capturing more planes

## Slide 3: Needed Methods
Generate FM array [x kinda]
Generate super pixel array(sp_y, sp_x, channel) [x]
Image subdivider [x]
Integrate image into super pixel array (image, channel) [x]
Tile chooser [x]
Auto Focus(channel)
Well Depth filter
Focus prediction populator
Plane fitter
Plane 2 FM map

## Slide 4: FM Array Constructions
9
Number Z slices A647 with depth of focus step sizes
8
Top Z position A647
7
Number Z slices A555 with depth of focus step sizes
6
5
4
3
2
1
0
X positions
Y positions
Top Z position DAPI
Number Z slices DAPI with depth of focus step sizes
Number Z slices A488 with depth of focus step sizes
Top Z position A555
Top Z position A488
Contains all channel info
Numpy array with dimensions (10, y_tiles, x_tiles). X and Y tile count come from Micro Magellan array
Dtype = int16

## Slide 5: Super Pixel Array Array Constructions
4
3
2
1
0
[Reciprocal Brenner Score plane 1, Z position]
[Reciprocal Brenner Score plane 2, Z position]
[Reciprocal Brenner Score plane 3, Z position]
[Predicted Focus Z position, Nothing]
Super Pixel Mask
[All pixels 0 or 1, Nothing]
1 Array per channel.
Numpy array with dimensions (5, y_super_pixel_count, x_super_pixel_count, 2).
y_super_pixel_count = int(super_pixels+per_image * y_tile_count *overlap_adjuster)
Dtype = float64

## Slide 6: Auto Exposure Algorithm
Start from 100ms exp time
Go to XY tile position
  Take image with given channel
  Check if image is within bounds at the 99% percentile pixel
    If saturated
      reduce exp time by 10x
      retake image and recheck if still saturated.
      Repeat 1-2 until not saturated anymore
      Scale exp to give 10% dynamic range intensity
    If too low
      Scale exp to give 10% dynamic range intensity or 1000ms, which ever one that is lower exposure time
  If not saturated add to exp_calc_array and move to next z point
  Repeat steps 1-4 until all 3 z points are acquired w/ same exp time. Must retake images if needed
  Repeat steps 1-5 until all 4 channels are set
Repeat for all XY position with starting exp time being rolled over from previous XY position
Solve quadratic equation for all three intensity points via gauss Jordan reduction method to solve for all coefficients.
Find intensity that is predicted via derivative of quad equation set to zero and subbed back in.
Cycle through all results as a function of XY position to find the highest predicted intensity after being scaled by exp time.
Take desired intensity/highest intensity to make a scale factor
Take acquired exp time and multiply by new scale factor.
  If new exp time > 2000ms, make = 2000
  If less than 2000ms, don’t alter new exp time

## Slide 7: Auto Expose Array Construction
3
2
1
0
[X percentile intensity in image 1, Z position, exp_time ]
[X percentile intensity in image 2, Z position, exp_time ]
[X percentile intensity in image 3, Z position, exp_time ]
[Predicted in focus intensity, predicted focus]
1 Array per channel, delineated by index and not file name
Numpy array with dimensions (4 (channels), y_tiles, x_tiles, 4, 3).
Dtype = Int16
3
2
1
0
[X percentile intensity in image 1, Z position, exp_time ]
[X percentile intensity in image 2, Z position, exp_time ]
[X percentile intensity in image 3, Z position, exp_time ]
[Predicted in focus intensity, predicted focus]
3
2
1
0
[X percentile intensity in image 1, Z position, exp_time ]
[X percentile intensity in image 2, Z position, exp_time ]
[X percentile intensity in image 3, Z position, exp_time ]
[Predicted in focus intensity, predicted focus]
3
2
1
0
[X percentile intensity in image 1, Z position, exp_time ]
[X percentile intensity in image 2, Z position, exp_time ]
[X percentile intensity in image 3, Z position, exp_time ]
[Predicted in focus intensity, predicted focus]
DAPI = index 0
A488 = index 1
A555 = index 2
A647 = index 3

## Slide 8
5.6 seconds for all processing with 12 tiles

## Slide 9: Autofocus
New auto focus will utilize the 3 images from autofocus and project out what the approximate ideal exposure would be.

## Slide 10
Plot highest int value of the bottom 99% pixels vs slice in image array
Also plot 1/highest pixel
Plot z slices 7-22 and fit reciprocal to quadratic equation
Fits very well!
Chart: 99% Max int vs z slice
| 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22
 | 0.00014952 | 0.00014209 | 0.00013333 | 0.00012513 | 0.0001178 | 0.00011213 | 0.00010817 | 0.00010673 | 0.00010673 | 0.00010899 | 0.00011287 | 0.00011867 | 0.00012631 | 0.0001343 | 0.00014325 | 0.00015256

## Slide 11: Intertwining Auto Focus and Auto exposure
f
Find derivative