## Slide 1: Dye Kinetics H2O2 vs mCPBA vs LiBH4

## Slide 2: Protocol
Instrument = Tecan Spark
Sample holder = 96 well glass bottom plate
100uL sample per well
All ‘dyes’ are either secodnaries or direct primary antibodys
1:1k dilution on all dyes
Procedure
Mix all bleaching solutions
  24mM NaOH in PBS + 4.5% H2O2 (pH 9.5)
  10mM LiBH4 in MilliQ water
  1mM mCPBA in PBS, NaOH adjusted to pH 10
  24mM NaOH in PBS is referred to as bleaching PBS
Make Eppendorf of 1:100 diluted dye (150uL bleaching PBS + 1.5uL dye)
Dilute dye again in bleaching buffer at 1:10 for 100uL reference well
Add 315uL bleach solution into Eppendorf, add 35uL diluted dye solution, vortex, split 3 ways into wells for 100uL a piece
Repeat for other 2 solutions
Place into tecan and run procedure

## Slide 3: Tecan Procedure
Before measurements are taken, the z position is found with reference dye solution and fixed for rest of experiment
Go to reference dye, auto gain to make that 60% dynamic range
Record inverted fluorescence on every relevant well every 15 seconds
3 samples each condition

## Slide 4: Plate layout

## Slide 5: Filter/Settings each Dye
A488

## Slide 6: Tau Chart
No Significant Bleaching
No Significant Bleaching
No Significant Bleaching

## Slide 7: Notes
A488 H2O2, well E1 didn’t pipette well. Lower volume than expected.
H2O2 samples have lots and lots of bubbles. This will affect kinetic readings stochastically.
Weighed everything in containers that they were mixed in.