## Slide 1: Changelogs

## Slide 2: V3.1
Filleted lengthwise inner edges of oring channel for inner chamber and inner chamber socket to improve printing quality.
Fixed parameter where oring channel height was not being adjusted for inner chamber
Increased port diameter for inner chamber from 4mm – 4.8mm to accomodate screw in quick turn module.
Inner chamber and socket oring channel depth decreased to 2.6mm
Widened gap between socket walls and inner chamber walls from 0.5mm to 0.7mm
Adjusted corner fillets for all channels (socket and oring) to have even thickness as it curves
Lengthened inner chamber socket’s width and length to 130 and 52mm from 125 and 45.
General tweaks

## Slide 3: V 3.2
Changed gap reference from slide well on outer chamber to slide window on inner
Made port to slide window on inner chamber asymmetric in order to shrink inner chamber window and have area where protrusion can exist above frosted part of slide
Slide window is inset 18mm on frosted side w/ respect to slide well
Increased gap from port to slide window edge from 5mm to 10mm and from 5mm to 28mm on the frosted side
Mounting screw differences were actually 148.5mm and 98.5mm. Seems to have undershot by 1.5mm. Increased gaps to 151.5 and 101.5 respectively.
Hexnut was a tad loose. Decreased socket diameter from 8.7 to 8.5mm.
Primary objective on this revision is to increase FEP window robustness on inner chamber and create a protrusion on the portion directly over the frosted label on the slide. This will press down onto that portion and keep it in place during acquisitions.

## Slide 4: V3.3
Shrunk overall dimensions to smallest possible over the slide to reduce volume of fluid needed.
Shrunk slide well length from 26mm to 25.8 to slightly tighten socket.
Shrunk inner socket width and length from 130mm and 55mm to 105 and 42mm.
Port cutout width changed from 15mm to 6mm
Fluid height reduced from 0.2mm to 0.1mm
Port to slide well gap reduced from 10mm to 3mm.
Port riser side dropped from 10mm to 9mm
Inner socket oring height above ground increased from 3mm to 4.5mm.
Added in part to calculate projected fluid volume needed
Reduced gap between mounting screw and hexnut from 6mm to 3mm
Reduced outer chamber width and length from 165mm and 85mm to 130mm and 60mm
Reduced mounting screw separation length and width from 126.5 and 101.5 to 126.5 and 76.5mm
Reduced mounting plate width and length from 115mm to 90mm (width scaled with outer chamber width as width plus 2mm.
Reduced outer chamber wall thickness from 10mm to 8mm.
Overall needed fluid volume dropped from 1.3mL to 0.35mL
Glitched in chamfering inner socket (actually chamfered bottom part, but this should effect much).

## Slide 5: V3.4
Expanded out inner socket fillets to get a better oring seal. I will also eliminate the top part of the inner socket oring socket. Additionally, remove oring from inner chamber and reduce inner socket chamber width
Fixed order of operation (ie make inner before outer) for channel and socket fillets
Eliminate slide protrusion
Changed innersocket fillet to 20mm
Changed oring fillet to 13.7mm.
Changed socket thickness to 4mm
Altered length and width of both the outer chamber and inner chamber socket
Removed oring from inner chamber

## Slide 6: V3.5
This is a major change. Lateral oring was swapped for a compression gasket that is laid on the slide’s face. Gasket will be made from parafilm which is around 100-120um thick. Second major change was to make the inner chamber a two part system and made a kinematic mount for it. Its not super exact, but inner chamber tilt was anticipated to be the most important part. Centering magnets should get within micron ranges which is more than sufficient to get the slide tilt within 50% the depth of View which is 1 micron over a FOV.
Swapped inner chamber to be a two piece system with 6 screws for compression. Both hexnuts and heads are all inset
Made slide 0.5mm higher in socket so that slide surface is higher than anything else on bottom inner chamber so then the upper portion will contact it first, making compression with a gasket possible.
Made kinematic mount with two sets of centering magnets. Magnets mounted with screws and outer chamber has inset deep enough to hold both magnets with a gap between to weaken them around 2 fold. Tracks with magnets are longer than need be so the inner chamber can be shifted to one side to break mag bond better and more easily.
Rebuilt entire CAD model to generate this V 3.5 model.