## Slide 1: Slide Bleach Analysis

## Slide 2: Outline
Stained and bleached slides
cycle 0
1:5k hoescht 5 minutes
cycle 1
Primary
1. Mouse-ECAD
2. Rabbit-MUC2
Secondary
1. anti-mouse-488
2. anti-rabbit-532
cycle 2
1. ezrin-488
2. chromogranin A -A594
3.gamma actin-A647
cycle 3: this cycle was done the following day.
1. PCNA -A488
2. villin-A546
3. Na-K-APase- A647
Primary incubation 1:100 for both for 45 mintutes
Bleach solution was 10mM m-CPBA in PBS at pH 10.
Bleach incubation time was 5 min
2X washes w/ pbs after bleach time was over
4x4 binned images

## Slide 3: Green Channel
Cycle 1 Ecad-A488
Cycle 2 Ezrin-A488
Cycle 3 PCNA-A488
Cycle 3 bleach
Stained
Bleached

## Slide 4: A488
RAW
Masked

## Slide 5: A488 intensity vs cycle (and bleach count)
Mask used in cycle 1 is same as mask used for cycle 1 bleach image.
Mask in cycle 2 is same as cycle 2 bleach, etc.
Number is reported avg from histogram in imagej
Note signal includes autofluorescence in all numbers including bleached signal as I messed up initial unstained image
Chart: Signal after stain and bleach % comparision
| cycle1 | cycle2 | cycle3
Bleached Signal | 553 | 710 | 558
Stained Signal | 4734 | 23945 | 4248

## Slide 6: Red Channel Notes
Strange pattern on Image that I couldn’t figure out why it was there at the time. After diagnostics, I determined that it was a reflection pattern on the ring above the platform that hold the objective and moves it.
Chromogranin A has not worked in a long time. So it not showing up is not surprising
Villin-A546 has never been tested in my hands before. Unknown if it will stain if it is the first one chosen. Villin-A488 stains very well though.

## Slide 7: Red Channel
Stained
Bleached
Cycle 1 Muc2-A532
Cycle 2 Chromogranin A-A594
Cycle 3 villin-A546

## Slide 8: Far Red Channel
Stained
Bleached
Cycle 1 -Nothing
Cycle 2 Gamma Actin-A647
Cycle 3 Na/K ATPase-A647

## Slide 9: Hoescht Bleaching
Cycle 2
Cycle 2 Bleach

## Slide 10: Notes on experimental rerun
Use curtain to stop reflection pattern
Take image before even Hoescht stain is applied
Use 1x1 (if RAM is finally in)
Lower exposure times on autofluoresced image and scale to subtract
Make sure not to alter location
Level slightly better (its close to being good enough)
Use A555 for the first cycle secondary