## Slide 1: Pressure Calculations for AutoCIF Micro-Fluidic Device

## Slide 2: Microfluidic Chip AutoCIF
Use window dimensions from GeoMx® Digital Spatial Profiler
Use extended channels as port canals to move ports away from window.
Main chamber slightly narrows to encourage bubbles to not stick
Ports funnel, remove sharp transitions and have rounded backs

## Slide 3: Block Hydraulic Resistant Diagram
Fluidic Chip
ID: 500um, L:20cm
ID: 500um, L:100cm
ID: 500um, L:200cm
ID: 500um, L:50cm
ID: 1600um, L:1000cm
R1 =0.02
R2 =.11
R3 =.22
R4 =0.05
R5 =0.01
Resistance Units = [torr*min/uL]
R_Cell =0.01

## Slide 4: Equivalent Component Model
Pressure = Voltage
Flow Rate = Current
Tubing and Chambers Hydraulic resistance = resistors

## Slide 5: Peristaltic Pump Equivalent
While true, they are not perfect flow generators. If backpressure is low as compared to max pressure, then it is approximately a constant flow rate generator.
Given knowledge of absolute flow rates are not imperative in this operation, a 1st order approx. is valid
Peristaltic pump equivalent electrical component is thus a constant current source PSU.

## Slide 6: Calculating Approximate PSI Max on pump
At 3200uL/min is about 1200 RPM
We currently run at 12V
Running Torque is then 0.06Nm
Drive axle = 5mm
Pump head = 23mm
Assuming friction and tube compression eat up 50% of the theoretical max torque and starting torque is 50% lower than stopping torque. Max torque = 0.015Nm
Max force at tubing = 1.3N
Back pressure force = Back_Psi*CSA(0.007) = .0014*back_psi N
Max back pressure force = 1000psi
Max psi on tygon 1/16 tubing = 145psi
Max psi bubble trap = 30 psi
Seems a lot high even though it makes sense.

## Slide 7: Electrical Equivalent Circuit
At 3.2mL/min flow rate, peak system pressure = 1344 torr and chamber peak pressure = 64 torr
At 1mL/min flow rate, peak system pressure = 420 torr and chamber peak pressure = 20 torr

## Slide 8: Other performance features
Tubing volume = 73uL. Chamber volume = 71uL. Lag time of type of fluid exchange is 144/3200 = 2.7 seconds
Tubing volume = 73uL. Chamber volume = 71uL. Lag time of type of fluid exchange is 144/1000 = 8.64 seconds
Peak pressure on pump at 3200uL/min = 26 PSI.