## Slide 1: Compressing Folder Sets

## Slide 2: Example Case: Casey Slide 1-21-25
Original size = 131gb
3 z-stacks and HDR inspired auto exposure
12 tiles, 8 cycles (9 with autofluorescence)
Deletion: all 3 z stacks (keep infocus ones aka focus folder), basic folder, basic_df, stage placed images, nuclear binary, tissue binary (retain only labelled tissue image).
Compressed w/ zlib: focused images, bleached images, mcmicro files

## Slide 3: Size Drop Going from 3 stack to single FOV.
Original: 131gb
After deletion of stained 3 stack for stain: 89gb
Bleached 3 stack to 1 stack = 14.5gb

## Slide 4: After different actions
Space saved deleting basic and basic_df folders for each color and cycle = 26gb
Saved compressing single plane stain and bleach only images = 13gb
Compress data structures and delete quicktile = 3.5gb

## Slide 5: Overall Folder Size Reduction
Start with 3 stack to single stack and all above reductions = 131gb to 25gb, 19% original size
0.23gb*tiles*(cycles + 1)= final folder size; +1 is autofluorescence
50 tile dataset ala GutAge = 126gb

## Slide 6: Archiving Folder Sets
Each dataset will contain 2 folders. Here are each folders contents:
Folder 1 (McMicro):
Stitched final images
Folder 2:
Single copy of all raw (post HDR) images from every channel and for both stain and bleach